## Slide 1: FlipPhone Software Design
https://github.com/kjjl/flip-phone

## Slide 2: Background
FlipPhone Control Software (FCS) is loaded onto FlipPhone device to:
  Detect fall
  Determine fall parameters
    Angular orientations
    Angular velocities
    Height from ground
  Predict time until impact
  Predict angular orientation at impact
  Determine reaction wheel (RW) rotation ramp to control impact angular orientation
  Run RW
  Detect impact

## Slide 3: State Machine
Boot Up
Standby
Off
Device switched “On”
Initialization
Initial Distance Acquisition
Fall detected
Impact Forecaster
On time
Recovery Calculator
On time
On time
Engine Controller
Impact Detector
On time
Impact detected
Time Expired
Late
Late
Late
Late
Late

## Slide 4: Software Requirements Mapping
Requirement | Standby | Distance Acquisition | Impact Forecaster, Recovery Calculator | Engine Controller | Impact Detector
(M) time | X | X | X | X | X
(M) acceleration | X |  |  | X** | X
(M) orientation | X | X |  |  | X
(M) angular vel. | X |  |  |  | X
(M) distance |  | X* |  |  | 
(B) dist. table |  | X* |  |  | 
(R) dist. table |  | X | X |  | 
(E) impact time |  |  | X |  | 
(E) impact angle |  |  | X |  | 
(C) RW params |  |  | X |  | 
RW on |  |  |  | X | 
RW off |  |  |  | X | X
Data logger | X | X | X | X | X
(M) – Measure, (B) – Build, (R) – Read, (E) – Estimate, (C) – Calculate, * - Threaded, ** - Unsure

## Slide 5: Standby
Continuously read:
  Time
  Acceleration
  Orientation
  Angular velocity
When relative 0 G is detected, save to a variable the latest:
  Time
  Acceleration
  Orientation
  Angular Velocity
When relative 0 G is detected, move to Initial Distance Acquisition state

## Slide 6: Time Expired State
Return to Standby state

## Slide 7: Initial Distance Acquisition
Using time, orientation, and angular velocity at 0 G, generate a table of time and predicted orientation.
Continuously read:
  Time
When time matches time at which predicted orientation is facing ground, ping distance and save to an array of tuples the latest:
  Time
  Distance
If a minimum number of distances are recorded before a timeout, move to Impact Forecaster state. Otherwise move to Time Expired state

## Slide 8: Generate Time-Predicted Orientation Table
Given initial rotation speed and initial orientation matrix: we can propagate orientation to the end of the maneuver:
Propagation from time point to :
Compare angle between for propagated and real for just the z axis
Also see reference:
  http://www.mare.ee/indrek/varphi/vardyn.pdf

## Slide 9: Impact Forecaster
Using time and distance from Initial Distance Acquisition state, find height and velocity at 0 G:
  Given measurement vector:
  At times: . Notice
  We shall use the following equation to estimate :

## Slide 10: Impact Forecaster
Using height and velocity at 0 G, find time until impact:
  Where
    - fall start reference time (g acceleration lost)
    - impact time (g acceleration re-gain)
    - height at fall start ()
    - vertical velocity at fall start (if falling down )
    – gravity acceleration

## Slide 11: Impact Forecaster
Using time until impact and time-predicted orientation table, identify orientation at impact.
If impact time and impact orientation have been determined and timeout has not been exceeded, move to Recovery Calculator state. Otherwise, move to Time Expired state.

## Slide 12: Recovery Calculator
Given initial orientation, initial angular velocity, time until impact, and predicted impact angle, calculate RW ramp to change impact orientation to be within safe zone.
If timeout has not been reached, move to Engine Controller state. If timeout has exceeded, move to Time Expired state.

## Slide 13: Calculate RW Ramp

## Slide 14: Engine Controller
Send RW ramp instructions to engine.
If timeout has exceeded, move to Time Expired state.